## Slide 1: RC Interpolation vs. RC Smoothing
Code Location: https://github.com/betaflight/betaflight/blob/master/src/main/fc/fc_rc.c

## Slide 2
Debug_Mode = RC_Smoothing
  debug(0) = raw un-smoothed rc channel data
  debug(1) = raw un-smoothed setpoint derivative
  debug(2) = filtered setpoint derivative before applied to setpoint weight
  debug(3) = auto-calculated filter cutoff frequency base after sampling the rx frame rate
Debug_Mode = RC_Smoothing_Rate
  debug(0) = log each RX frame interval
  debug(1) = log the training step count
  debug(2) = the current calculated average
  debug(3) = indicates whether guard time is active
Debug_Mode = RC_Interpolation
  debug(0) = raw un-smoothed rc channel data
  debug(1) = current RX frame rate

## Slide 3: Interpolation
Advantages:
Simple
No Pumping Effects
Disadvantages:
Delayed 1 frame rate
Handles dropped frames poorly
Abrupt Changes in Slope
Input Delayed = to Frame Rate+
Abrupt Change in Slope = Problematic

## Slide 4: Interpolation
Abrupt Changes in Slope
D-term Jerk
D-term Jerk

## Slide 5
Interpolation set to Manual = 15ms for a 22ms frame rate

## Slide 6: RC Smoothing
Advantages:
Less delay (ascending leg)
Smoother Edges (no juts)
Less affected by loop-time jitter
Handles packet loss better.
Disadvantages:
Reseeding Leg has more Lag
Less Leading Lag
More Trailing Lag
Pull Request: https://github.com/betaflight/betaflight/pull/6017

## Slide 7: RC Smoothing Calcs
Hz = 1/ ([ms of latency] /1000)
  E.g: 1 / (22ms / 1000) = 45.5hz
[Frame rate in Hz] / 2 x 90% = cut-offs
  E.g.: 45.5 / 2 x 0.9 = 20hz
  Command “rc_smoothing_info”
  to get RX rate to FC

## Slide 8: Special RX / TX Conditions
SBus or FPort users
  set their radio link to D16 mode and no more than 8 channels
Spektrum (DX6i, DXe, DX6e)
  RX at 11ms (91hz), but TX sends at 22ms (45hz)
  read this document for setting up RC Smoothing Filter correctly (manually)
Crossfire
  150hz (6.7ms) to 50hz (20ms) to switching
  https://github.com/betaflight/betaflight/issues/6239
  Debug_mode = RC_SMOOTHING_RATE

## Slide 9: Other Pull Requests
Details on Crossfire 50hz to 150hz Challanage:
  https://github.com/betaflight/betaflight/issues/6103 (discusses issue in Interpolation as well)
  https://github.com/betaflight/betaflight/pull/6194 (adding full support of CRSF)
  https://github.com/betaflight/betaflight/issues/6239 (RC5 improvements)
Proposed RC_Interpolation Advanced by Plasmatree
  https://github.com/betaflight/betaflight/issues/6112